## Slide 1: Detecting consistent common lines in cryo-EM by voting
Szu-Chi Chung
Institute of Statistical Science, Academia Sinica

## Slide 2: Projection-Slice Theorem (3D)
2D projections from the same 3D object share a common line
Finding common line:
Calculating similarity in Fourier space using radial line
Notes: https://embo2017.cryst.bbk.ac.uk/embo2017/course/Lectures/Lecture%2013%20-%20Sjors%20Scheres_p4.pdf
Fourier space following is easy:
Convolution, filter, Cross correlation
Linear model

## Slide 3: Projection-Slice Theorem (2D)
2D
1D
Finding common line:
Calculating similarity in Fourier space using radial line
Calculating similarity in real space using Sinogram line (projection line) - Faster
Notes: https://www.researchgate.net/figure/Central-slice-theorem-the-1D-Fourier-transform-of-a-Radon-projection-at-angle-0-is_fig11_222275232
Fourier transform is a unitary operator

## Slide 4: Radon Transform
Parameterizing Parallel-Beam
Radom transform
Projection-Slice Theorem [1]
Notes: Dirac delta function
Note that [0; 180] captures all necessary projections of the object. The angular range [180; 360] gives a \mirror image.“
In addition to the Poisson noise discussed previously, data can be affected by numerous other issues.
- Detector noise.
- Scatter (some X-rays do not follow straight line).
- X-rays are not monochromatic, but have full spectrum. Attenuation
coefficient depends on energy ! beam hardening.
- Bad detectors, e.g., void measurements.
- Too dense features in the object, e.g., metal blocking rays completely.
- Object changing during acquisition, e.g., motion.

## Slide 5: Radon transform [1,2]
Sinogram
  Projection
  Radom transform
  0 degree
  5 degree

## Slide 6: Angular reconstruction in cryo-EM [3]
Projection-Slice Theorem Common Line
  Number of good common lines needed for assigning the Euler angles of projections is (Note that we have common lines)
Angular Reconstruction (method that using common line detection)
  IMAGIC, Spider, Xmipp, Aspire
Notes: Only obtain initial model, since it can not iterative refine (when SNR is low do single run will not be accurate)

## Slide 7: Detection of common line
Heterogeneity
  Common line similarity can also be used to differentiate conformations
Sensitive to noise
  The common line detection rate decrease steeply when SNR decrease (e.g. SNR level 0.5 be a phase transition point)
    In the literature, the 2D classification or 3D angle partition are usually employ to boost the SNR
    Use network to simultaneously consider many projections
From here

## Slide 8: Idea of voting [4]
Consider the case where the common line between two projections pair is correct
  All other projections should determine the angle with probability
  Thus there are good projection k that vote for
  All the others ) should vote to random or results in non-physical angles
If between two projections are incorrect
  All projection should vote to random or results in non-physical angles (Note that we have radial lines)
  Correct
  Incorrect
If , we can distinguish correct and incorrect common line (Note )

## Slide 9: Non-physical angle
Build common line matrix
The directional vector of each radial line are the radial line of unit sphere
  The intersections of three projections are denoted as
  They must satisfy the following inner product
Notes: https://math.stackexchange.com/questions/73237/parametric-equation-of-a-circle-in-3d-space

## Slide 10: Non-physical angle
Assume we place projection 1 on x-y plane and let
  By we get
Projection 2 can be written as (using and as unit vector)
  =
  From we get since is on projection 2, we get
  From we get the condition of physical angle
Notes: https://math.stackexchange.com/questions/73237/parametric-equation-of-a-circle-in-3d-space
Red green blue

## Slide 11: Voting algorithm
Record peak
Verify condition
Add to histogram
Build common line matrix

## Slide 12: Voting and filtering
Retain only percent tile
of highest correlation or peak
Only histogram filtering
improves with
Voting can improve the accuracy in given SNR and can get benefit from increasing sample size

## Slide 13: Voting and filtering
The choice of threshold
  Plot histogram of all peaks (use as threshold)
  Experiment data use (, remember that )

## Slide 14: Apply to network (data from [5])
Filtering common lines
  Use peak instead of
  common line similarity
  to construct graph?
Test with different structures
  Direct distinguish structure without
  graph clustering?
Peak
Different structure
Same structure
Common line similarity

## Slide 15: Reference
[1] http://www2.compute.dtu.dk/~pcha/HDtomo/SCforCT.html
[2] https://scikit-image.org/docs/dev/auto_examples/transform/plot_radon_transform.html
[3] Wang, Lanhui, Amit Singer, and Zaiwen Wen. "Orientation determination of cryo-EM images using least unsquared deviations." SIAM journal on imaging sciences 6.4 (2013): 2450-2483.
[4] Singer, A., Coifman, R. R., Sigworth, F. J., Chester, D. W., & Shkolnisky, Y. (2010). Detecting consistent common lines in cryo-EM by voting. Journal of structural biology, 169(3), 312-322.
[5] Verbeke, E. J., Zhou, Y., Horton, A. P., Mallam, A. L., Taylor, D. W., & Marcotte, E. M. (2020). Separating distinct structures of multiple macromolecular assemblies from cryo-EM projections. Journal of structural biology, 209(1), 107416.
[6] 2D implementation of Relion and CryoSparc https://github.com/Arunabh98/EPFL-CryoEM

## Slide 16: Appendix

## Slide 17: Introduction
Using 2D images to obtain final 3D density maps
  Determine the relative orientations
    Euler angles θ, ϕ, , ,
  Use existing 3D reconstruction methods
      (a) Direct Fourier Reconstruction
      (b) Weighted back-projection
      (c) Algebraic Reconstruction Technique
Divide it into mainly two tasks
  Ab initial model generation
  3D classification and refinement

## Slide 18: Introduction
2D Fourier transform
Intensity vs frequency
Result is complex number
2D Shift
Notes: 1. Symmetric around original points!
2. Reference also see https://www.youtube.com/watch?v=nyk75ufbP74&t=0s&index=18&list=PL8_xPU5epJdctoHdQjpfHmd_z9WvGxK8-

## Slide 19: Reconstruction from Sinogram [1,2] (Tomography)
Simultaneous Algebraic Reconstruction Technique (SART)
Filtered Back Projection (FBP or WBPJ)
Notes: https://www.int.kit.edu/1731.php

## Slide 20: Reconstruction from unknown angles [6]
RELION (ML-EM)

## Slide 21: Reconstruction from unknown angles [6]
CryoSparc (Gradient descent)

## Slide 22: Filtered Back Projection
Using Fourier Slice Theorem
Projections are filtered by multiplying with the
ramp filter in the Fourier domain.
Notes: https://mathinsight.org/double_integral_change_variables_introduction#mjx-eqn-cvarformula

## Slide 23: Filtered Back Projection
To compute FBP reconstructed image from projections:
  Fourier-transform each projection (1D Fourier transform).
  Apply ramp filter by multiplication with (High pass)
  Optionally, apply additional low-pass filter to handle noise.
  Inverse Fourier-transform to obtain filtered projections.
  Backproject the filtered projections and sum up
In practice we do not have all and since we record a finite number of projections with a detector of fixed size.
Interpolation from polar to Cartesian grid, known as “regridding," is required for 2D inverse Fourier transform and difficult.
Fourier method is seldom used in practice.

## Slide 24: Algebraic Reconstruction Technique

## Slide 25: Algebraic Reconstruction Technique
Cimmino’s method accesses the rows simultaneously and computes the next iteration vector:
Notes: Karczmarz, Cimmino and similar algebraic iterative methods are usually considered as solvers for systems of linear equations.
But it is more convenient to consider them as optimization methods.
Within this framework we can easily handle common extensions: